## Slide 1: BIOS Update and Failure Scenarios
A comprehensive overview including process, risks, failures, and diagram.

## Slide 2: How BIOS Updates Work
Rewrites firmware in flash memory.
Includes boot firmware, ACPI tables, microcode patches, and platform-specific code.
Steps: Run update tool → Verify image → Flash firmware → Reboot & POST.

## Slide 3: Reasons for BIOS Updates
Support for new CPUs, GPUs, and memory modules.
Fix ACPI table and power state issues.
Improve stability and OS compatibility.
Patch security vulnerabilities.
Optimize power and thermal control.

## Slide 4: Common Failure Scenarios
Flashing failures: power loss, wrong image, buggy update tool.
Post-update failures: ACPI mismatch, driver issues, hardware instability.
Changed power/thermal settings causing sleep/hibernate issues.

## Slide 5: Risk Factors
Older systems without recovery features.
Laptops with tightly integrated firmware.
Complex server stacks (BIOS + BMC + CPLD).
Overclocked or modified hardware.

## Slide 6: Mitigation & Recovery
Backup firmware and ensure stable power.
Update related components (Intel ME, BMC).
Check release notes for ACPI or microcode changes.
Recovery: Dual BIOS, recovery mode, SPI programmer, or vendor RMA.

## Slide 7: ACPI-Specific Failures
Boot failure due to missing/malformed ACPI tables.
Broken CPU scaling, battery reporting, or thermal control.
Virtualization failures due to corrupted IOMMU/IVRS tables.

## Slide 8: Summary Table: Failures and Symptoms
Stage | Issue Type | Example Symptom
Flashing | Power loss during update | System won’t POST
Flashing | Wrong image | Bricked system
Post-update | ACPI table mismatch | OS won’t boot or ACPI error
Post-update | Driver incompatibility | Devices missing or malfunctioning
Post-update | Microcode incompatibility | Reboots or performance issues
Post-update | Changed power/thermal settings | Sleep/hibernate fails