## Slide 1: EDA on HPC: Interview Briefing
Workload patterns, performance tuning, and a real-world case study

## Slide 2: Problem Framing and Goals
Goals
  Shorten tape-out cycles and reduce re-spins
  Increase throughput of regressions and sign-off
  Control license and infrastructure costs
Primary Constraints
  License tokens (FlexLM/RLM) and denial rates
  I/O hotspots on shared filesystems
  Long-running solver jobs and queue contention
Success Metrics
  Time-to-first-useful-result, nightly regression pass rate
  Sign-off wall time, queue wait < targets
  Cost per successful tape-out milestone
Notes: Open with the problem you solve and how you measure success.

## Slide 3: EDA Workload Taxonomy (Scale Indicators)
Digital Verification
  RTL/UVM: 10k–1M tests/night; 1–8 cores/test; high small-file I/O
  Gate-level + SDF: 4–32 cores; heavy waveforms; 2–24h runtimes
Physical Implementation
  Synthesis: CPU-bound; 32–128 cores; 64–512 GB RAM
  P&R: memory-bound; 64–256 cores; 256 GB–1 TB RAM
Sign-off & DFM
  STA (MMMC): thousands of views; embarrassingly parallel
  DRC/LVS: geometric tiling; 500–5000 cores; TB-scale GDS/OASIS
  Extraction/IR/EM: solver-heavy; CPU+GPU; long wall times

## Slide 4: Parallelization Patterns That Work
Embarrassingly parallel: regressions, STA views, corner sweeps (job arrays)
Data partitioning: DRC/OPC/litho, extraction (tile size vs halo overlap)
Hierarchical decomposition: block-level STA/P&R; promote deltas only
MPI/distributed solvers: EM/thermal; needs low-latency fabric and CPU affinity
Pipeline parallelism: synth → P&R → STA → sign-off with dependencies

## Slide 5: Reference HPC Architecture for EDA
Compute
  CPU nodes: 2×64c with 1–2 TB RAM; GPU nodes for solvers
  Per-node NVMe scratch for hot artifacts
Scheduler
  LSF/Slurm/PBS with license-aware wrappers
  Job arrays, dependencies, quotas, and fair-share
Storage
  Lustre/GPFS/BeeGFS for shared design DBs
  Read-only caches for PDKs and techfiles
Network
  InfiniBand HDR/NDR or tuned RoCEv2
  <2 µs latency target for distributed solvers

## Slide 6: Storage and I/O Engineering
Parallel Filesystems
  Stripe large read-mostly files (count 8–32, size 1–8 MB)
  Separate metadata and data paths; avoid metadata storms
Per-Node Scratch
  Use local NVMe; checkpoint and copy back at milestones
  Compress/prune waveforms; set retention windows
Small-File Problem
  Bundle tiny artifacts (tar/SQLite/LMDB) to reduce inode pressure
  Prefer append-only logs; chunk artifacts for prefetchers

## Slide 7: Network and Host-Stack Tuning
InfiniBand or tuned RoCEv2; enable ECN/PFC only where needed
NUMA and CPU pinning; isolate NIC IRQs; housekeeping cores
TCP rmem/wmem autotuning; avoid bufferbloat on shared links
GPU-direct RDMA: validate drivers/firmware and IOMMU settings

## Slide 8: License Engineering + Scheduler Policies
Licenses
  HA FlexLM/RLM; monitor token pools and denials
  License-aware submission; exponential backoff on checkout
Policies
  Queues: debug, normal, tape-out priority, long-running solvers
  Backfill, reservations, and per-user concurrency caps
Utilization
  Bin-pack jobs with complementary feature bundles
  Fair-share, borrow windows, and preemption for tape-out

## Slide 9: Cloud Burst Playbook
Data gravity: keep compute near PFS (FSx Lustre, ANF, OCI File Storage)
Cache warm-up: stage PDKs/libs/golden DBs to read-only caches/images
Spot/preemptible: enable checkpointing; mix on-demand for license-heavy runs
Hybrid licensing: split entitlements; apply guardrails and budgets
Cost controls: idle shutdown, per-flow budgets, artifact TTL

## Slide 10: Observability and SLOs
What to Track
  Per-job CPU, RAM, I/O, license wait; queue times and denials
  Metadata ops/sec, OSS/OST utilization, top talkers
Dashboards & Alerts
  Grafana views for hot spots and denials
  Auto-triage: I/O saturation vs CPU starvation suggestions
SLO Examples
  Queue wait < 15 min for debug; < 60 min for sign-off
  Nightly regression completion > 95%

## Slide 11: Case Study: 5 nm SoC Sign-off Acceleration
Context
  80M-instance SoC; flat top-level DRC/LVS; MMMC STA
  Hybrid on-prem + cloud cluster
Interventions
  DRC tiling with 10% halo; tuned tile size to >85% CPU
  Waveforms on NVMe; 72h retention; compressed
  Lustre stripe_count 8→24; stripe_size 4 MB
  License-aware wrappers reduced checkout retries 60%
Outcome
  Sign-off wall time down 37%
  Storage hotspots down 45%
  Stable license server load

## Slide 12: Readiness Checklist + Q&A
License-aware submission wrappers in place
Per-node NVMe scratch and periodic checkpoints
PFS striping profiles by file class; cache PDKs/techfiles
Backfill + tape-out priority queues with reservations
Dashboards for denials and metadata ops
Cloud burst playbook with staging and budgets

## Slide 13: Acronyms
Acronym | Meaning
EDA | Electronic Design Automation
HPC | High-Performance Computing
SoC | System on Chip
RTL | Register Transfer Level
UVM | Universal Verification Methodology
STA | Static Timing Analysis
P&R | Place and Route
DRC | Design Rule Check
LVS | Layout Versus Schematic
PDK | Process Design Kit
GDSII | Graphic Data System II (layout format)
OASIS | Open Artwork System Interchange Standard
MMMC | Multi-Mode Multi-Corner
SDF | Standard Delay Format
IR | Voltage drop on power network (IR drop)
EM | Electromigration
SPICE | Simulation Program with Integrated Circuit Emphasis
FastSPICE | Accelerated SPICE-class simulator
3DIC | Three-Dimensional Integrated Circuit
TSV | Through-Silicon Via

## Slide 14: Acronyms (continued)
Acronym | Meaning
IB | InfiniBand
RoCEv2 | RDMA over Converged Ethernet v2
RDMA | Remote Direct Memory Access
MPI | Message Passing Interface
NUMA | Non-Uniform Memory Access
IRQ | Interrupt Request
PFS | Parallel File System
NVMe | Non-Volatile Memory Express
Lustre | Lustre Parallel File System
GPFS | IBM General Parallel File System (Spectrum Scale)
BeeGFS | BeeGFS Parallel File System
LSF | Platform Load Sharing Facility
Slurm | Simple Linux Utility for Resource Management
PBS | Portable Batch System
FlexLM | Flexible License Manager
RLM | Reprise License Manager
SLO | Service Level Objective
SLA | Service Level Agreement