## Slide 1: ACPI Update Overview
Understanding Advanced Configuration and Power Interface (ACPI) Updates in Firmware and System Management

## Slide 2: What is ACPI
• ACPI (Advanced Configuration and Power Interface) defines how the OS interacts with hardware for power and configuration control.
• Enables power states (sleep, suspend, hibernate), thermal management, and device enumeration.
• ACPI lives within BIOS/UEFI firmware and provides tables the OS reads during boot.

## Slide 3: What is an ACPI Update
• An ACPI update modifies firmware-level ACPI tables or methods.
• Usually delivered as part of BIOS/UEFI or Embedded Controller (EC) firmware updates.
• Ensures compatibility with new OS versions, hardware, and power management features.

## Slide 4: Reasons for ACPI Updates
• Power management bug fixes (sleep/wake, suspend issues)
• Thermal control optimization (fan curves, temperature trip points)
• Battery reporting accuracy improvements
• Device enumeration or hot-plug fixes
• Security hardening and OS compatibility adjustments

## Slide 5: How ACPI Updates Are Delivered
1. BIOS/UEFI firmware update (main method)
2. Embedded Controller (EC) firmware update (indirect)
3. Operating system driver update (patching ACPI method behavior)
Most updates refresh DSDT/SSDT tables embedded in the BIOS flash.

## Slide 6: Step 1 – Preparation
• Identify current BIOS/firmware version.
• Review vendor release notes for 'ACPI' or 'power management' updates.
• Ensure stable power and maintenance window availability.
• Backup configuration settings and logs.

## Slide 7: Step 2 – Apply the Update
• Use OEM tools (fwupd, iDRAC, iLO, XClarity, BIOS flash utility).
• BIOS update refreshes ACPI tables: DSDT, SSDT, FADT, HPET, MADT.
• Do not interrupt power during flashing.
• System reboots to apply new firmware.

## Slide 8: Step 3 – Post-Update Validation
• Verify BIOS/ACPI version in setup or logs.
• Confirm improved sleep, thermal, and power control behavior.
• On Linux, inspect updated tables using:
sudo acpidump > acpi_tables.txt
• Test battery or fan control functionality.

## Slide 9: Rollback and Recovery
• Revert to previous BIOS version if regressions occur.
• Some systems support recovery mode or BIOS rollback.
• Keep previous firmware version files archived.

## Slide 10: Vendor Examples
Dell – BIOS update via Command Update or iDRAC
HPE – SPP/SUM or iLO firmware bundles
Lenovo – Vantage or XClarity
Intel – UEFI capsule or OFU tool
Supermicro – SUM or IPMItool through BMC

## Slide 11: Best Practices
• Always align BIOS and EC/BMC firmware versions.
• Review firmware changelogs for ACPI table changes.
• Test power states (S3/S4/S5) and thermal control after update.
• Track firmware changes in CMDB or version inventory.
• Perform updates during low-impact windows.

## Slide 12: Summary Diagram
ACPI Update Lifecycle:
Preparation → Firmware Download → Flash BIOS/EC → Reboot → Verify ACPI Tables → Validate Power/Thermal Behavior