## Slide 1: Relationship Between BIOS, BMC, CPLD, and ACPI
Understanding Firmware and Hardware Coordination in Modern Server Architectures

## Slide 2: Overview
These four components form the foundation of system management and control:
• BIOS/UEFI – Boot and initialization firmware
• BMC – Out-of-band management controller
• CPLD – Hardware logic controller for power/reset sequencing
• ACPI – Interface between BIOS and OS for power/thermal control

## Slide 3: System Hierarchy
┌────────────────────────────┐
│ Operating System │
│ (Linux / Windows / ESXi) │
└─────────────▲─────────────┘
│ ACPI Interface
┌─────────────┴─────────────┐
│ BIOS / UEFI │
│ Boot firmware & ACPI │
└──────▲─────────┬──────────┘
│ │
┌──────┴──────┐ ┌────────┴────────┐
│ BMC │ │ CPLD │
│Mgmt Ctrl │ │Logic Controller │
└──────────────┘ └────────────────┘

## Slide 4: Component Roles
• BIOS/UEFI: Initializes hardware, loads OS, exposes ACPI tables.
• BMC: Provides remote monitoring, power control, and telemetry.
• CPLD: Handles board-level sequencing, resets, fans, and GPIOs.
• ACPI: OS interface for power and thermal management defined by BIOS.

## Slide 5: BIOS and BMC Interaction
• BIOS reports system state and health to BMC during boot.
• BMC can initiate BIOS updates and track POST progress.
• BMC provides BIOS with telemetry data like fan speed and temperature.

## Slide 6: BMC and CPLD Interaction
• BMC issues power and reset commands via CPLD.
• CPLD handles voltage rail sequencing and board-level safety logic.
• BMC depends on CPLD signals to confirm stable board power before BIOS boots.

## Slide 7: BIOS and CPLD Interaction
• BIOS queries CPLD registers during POST for board health and status.
• CPLD communicates voltage, reset, and board revision data.
• BIOS relies on CPLD for proper hardware initialization timing.

## Slide 8: BIOS and ACPI Interaction
• BIOS generates ACPI tables (DSDT/SSDT/FADT) for the OS.
• ACPI methods define power states (S0–S5), sleep/wake, and fan controls.
• OS relies on ACPI to control hardware power and thermal behavior.

## Slide 9: Indirect Relationships
• BMC ↔ ACPI: Indirect; BMC manages sensors whose data ACPI exposes.
• CPLD ↔ ACPI: Indirect; CPLD enforces physical state transitions that ACPI triggers logically.
• BIOS ↔ BMC ↔ CPLD: Continuous coordination during boot and runtime.

## Slide 10: Power-On Sequence Example
1. BMC powers up first and checks PSU health.
2. BMC signals CPLD to enable power rails.
3. CPLD sequences voltage and reset logic.
4. BIOS starts execution once CPLD signals power good.
5. BIOS initializes devices and builds ACPI tables.
6. OS loads and uses ACPI to manage power and thermal events.

## Slide 11: Firmware Update Dependencies
Typical update order:
1. BMC → 2. CPLD → 3. BIOS (includes ACPI)
• Ensures lower-level controllers are stable first.
• Prevents timing or dependency mismatches between components.

## Slide 12: Analogy
Server as a car:
• CPLD = electrical relay and ignition logic.
• BMC = remote diagnostics and control system.
• BIOS = engine control unit that starts and configures the system.
• ACPI = the dashboard and controls through which the driver (OS) interacts.

## Slide 13: Summary Diagram
Firmware Control Relationship:
BIOS ↔ BMC ↔ CPLD form the foundation of system control.
ACPI is the software-visible interface bridging BIOS and OS.
Update dependency: BMC → CPLD → BIOS → ACPI.