## Slide 1: BIOS Update Procedures in a Server
Reliable, Secure, and Automated Update Process for Enterprise Systems

## Slide 2: Overview
• BIOS/UEFI initializes hardware during boot and sets up system firmware environment.
• Updates address security flaws, add hardware support, and fix compatibility issues.
• Failure can brick servers — reliability and rollback are critical.

## Slide 3: Step 1 – Preparation
• Identify target servers and current BIOS version (via IPMI/Redfish/CLI).
• Verify hardware compatibility and version dependencies.
• Ensure redundant power and low server load.
• Backup BIOS configuration (boot order, PXE, virtualization).

## Slide 4: Step 2 – Obtain and Validate BIOS Package
• Download BIOS image (.bin/.cap/.efi) from OEM site.
• Verify checksum and digital signature.
• Confirm correct model/board revision.
• Distribute via management tools (OpenManage, iLO Amplifier, XClarity).

## Slide 5: Step 3 – Staging and Initiation
Options:
1. In-band update via OS tools (fwupd, flashupdt, dcu-cli).
2. Out-of-band update via BMC or Redfish API (iDRAC/iLO).
• Out-of-band method is safer for remote servers.

## Slide 6: Step 4 – Flashing the BIOS
• Enter firmware maintenance mode.
• Erase old BIOS image from SPI flash.
• Write new BIOS image block-by-block with CRC validation.
• Dual-BIOS or backup partition ensures recovery.

## Slide 7: Step 5 – Verification and Reboot
• Firmware integrity validated using signature/hash.
• System reboots and verifies during POST.
• BMC records update logs in System Event Log (SEL).

## Slide 8: Step 6 – Post-Update Validation
• Check version via dmidecode, iDRAC/iLO, or Redfish.
• Verify BIOS settings and RAID/boot configuration.
• Perform hardware health checks after update.

## Slide 9: Rollback and Recovery
• Dual BIOS / Recovery jumper for redundancy.
• Automatic rollback on checksum failure.
• Manual recovery via USB stick or BMC restore option.

## Slide 10: Automation in Data Centers
• Redfish API or Ansible scripts for automation.
• Vendor tools: OpenManage, iLO Amplifier, XClarity.
• Canary rollouts and batch segmentation reduce risk.
• Integration with CI/CD and health gates.

## Slide 11: Best Practices
• Update BIOS and BMC together.
• Avoid concurrent updates on HA pairs.
• Maintain recovery media and version logs.
• Schedule updates during maintenance windows.
• Centralize firmware telemetry (Prometheus/ELK).

## Slide 12: Summary Diagram
BIOS Update Lifecycle:
Preparation → Validate → Stage → Flash → Verify → Reboot → Validate
Include safety rollback and monitoring loops.

## Slide 13: Vendor BIOS Update Tools Overview
Enterprise servers use vendor-provided management tools for reliable BIOS updates.
These tools support local, remote, and automated updates using BMC, APIs, or orchestration systems.

## Slide 14: Vendor Tool Comparison Table
Vendor | Tool(s) | Automation/API | Rollback/Recovery
Dell | iDRAC, OpenManage Enterprise, Lifecycle Controller | Redfish, Ansible, RACADM | Dual BIOS, iDRAC Recovery
HPE | iLO, OneView, SPP, SUM | RESTful API, OneView SDK, Ansible | SPP rollback, dual image recovery
Lenovo | XClarity, XCC, BOMC | XClarity REST API, Ansible | Backup BIOS, USB Recovery
Supermicro | SUM, SuperDoctor 5, IPMItool | Redfish, CLI, API scripting | Dual BIOS, USB recovery jumper
Intel | OFU, SSU, DCM | API-based orchestration | Recovery jumper, BIOS restore tool
Cisco | UCS Manager, CIMC, Intersight | Cloud API, CLI, REST | Rollback through UCS Manager

## Slide 15: Key Takeaways for BIOS Update Management
• Use centralized tools (iDRAC, iLO, XClarity) for consistent updates.
• Automate via Redfish, Ansible, or vendor SDKs for large-scale fleets.
• Always verify signatures and maintain rollback paths.
• Schedule updates via maintenance windows and log results centrally.