## Slide 1: BMC Firmware Update Procedure
Ensuring Reliable and Secure Management Controller Updates for Enterprise Servers

## Slide 2: Overview
• The Baseboard Management Controller (BMC) enables remote, out-of-band management.
• Updates deliver security fixes, new features, and improved stability.
• Improper updates can disrupt remote access — redundancy and validation are critical.

## Slide 3: Step 1 – Preparation
• Identify current and target BMC firmware versions.
• Verify compatibility with BIOS and CPLD versions.
• Ensure stable power and network connectivity.
• Backup configuration: user accounts, network settings, SSL certs, and alert rules.

## Slide 4: Step 2 – Obtain and Verify Firmware
• Download firmware image from OEM site.
• Validate checksum (SHA-256) and digital signature.
• Match firmware to board revision and BMC type (AST2600/AST2500).
• Check BIOS/BMC dependency matrix.

## Slide 5: Step 3 – Choose Update Method
Out-of-Band (Recommended):
- Dell iDRAC, HPE iLO, Lenovo XClarity, Supermicro BMC, Cisco CIMC.
- Use web UI, Redfish API, or CLI for upload.
In-Band:
- Execute via OS using vendor utilities (fwupd, dcu-cli, hpsum, SUM).

## Slide 6: Step 4 – Flashing the Firmware
• BMC enters update mode.
• New image written to SPI/NOR flash in chunks.
• CRC and signature validated before commit.
• Dual flash banks ensure rollback safety.
• Logs captured in SEL and vendor update logs.

## Slide 7: Step 5 – Activation & Reboot
• BMC restarts independently (no host reboot).
• Services (IPMI, Redfish, SSH) restart automatically.
• Sensors reload and firmware version committed.
• Temporary console outage (~2–3 minutes).

## Slide 8: Step 6 – Post-Update Validation
• Verify version via web UI, ipmitool, or Redfish.
• Confirm sensors, power control, and event logging.
• Validate remote KVM and alerting functions.
• Re-enable monitoring integrations.

## Slide 9: Rollback & Recovery
• Dual-image architecture enables rollback.
• Automatic fallback if verification fails.
• Manual recovery via USB stick, serial console, or jumper (Force Update Mode).

## Slide 10: Automation in Data Centers
• Centralized tools: Dell OME, HPE OneView, Lenovo XClarity, Supermicro SUM, Cisco Intersight.
• Use Ansible Redfish modules for scripting.
• Employ canary updates and staged rollout.
• Rollback and health validation after update.

## Slide 11: Best Practices
• Update BIOS and BMC in coordinated order.
• Use redundant network links for remote updates.
• Maintain version logs and recovery media.
• Automate using Redfish/Ansible APIs.
• Schedule during maintenance windows.

## Slide 12: Vendor Comparison
Dell – iDRAC, OME, RACADM, Redfish
HPE – iLO, OneView, Amplifier Pack
Lenovo – XClarity, XCC
Supermicro – SUM, IPMItool, SuperDoctor
Cisco – CIMC, UCS Manager, Intersight

## Slide 13: Summary Diagram
BMC Update Flow:
Preparation → Verify → Upload → Flash → Reboot → Validate → Monitor
Include rollback and automation paths visually.