## Slide 1: CPLD Firmware Update Procedure
Reliable Update Process for Complex Programmable Logic Device in Enterprise Servers

## Slide 2: Overview
• CPLD (Complex Programmable Logic Device) controls board-level power sequencing, reset logic, and low-level hardware coordination.
• Updates fix timing issues, add hardware support, or align with BIOS/BMC dependencies.
• Failure can affect power-up logic or fan control — reliability and validation are critical.

## Slide 3: Role in Server Architecture
• Acts as hardware glue logic connecting BIOS, BMC, VRMs, and sensors.
• Controls board power sequencing and reset timing.
• Interacts with BMC for firmware coordination.
• Non-volatile, retains configuration after power loss.

## Slide 4: Step 1 – Preparation
• Identify current CPLD version via BIOS, BMC, or CLI.
• Verify dependencies with BIOS and BMC firmware versions.
• Ensure stable AC power and network connectivity.
• Power down host OS before update.
• Backup configuration and version logs.

## Slide 5: Step 2 – Obtain and Verify Firmware
• Download from OEM (Dell, HPE, Lenovo, Intel, Supermicro).
• Validate checksum (SHA-256) and digital signature.
• Match firmware to exact board revision and CPLD type (e.g., AST2600).
• Check version matrix for BIOS-BMC-CPLD alignment.

## Slide 6: Step 3 – Staging and Initiation
Out-of-Band (via BMC):
• Use iDRAC, iLO, XClarity, or Redfish API to upload firmware.
• Example: racadm fwupdate -f cpld_update.bin
In-Band:
• Use vendor CLI from OS (fwupdate, SUM, sysfwupdt).
• System reboots to maintenance mode for flashing.

## Slide 7: Step 4 – Flashing the CPLD
• BMC halts power control logic and enters service mode.
• Old CPLD image erased; new image written in blocks.
• CRC and signature validation before activation.
• Logs recorded in BMC System Event Log (SEL).
• Do not power-cycle or reboot during flashing.

## Slide 8: Step 5 – Reboot and Validation
• System reboots automatically.
• CPLD initializes during power sequencing.
• Verify via BIOS setup or BMC firmware inventory.
• Check board health: power rails, fans, and temperature sensors.

## Slide 9: Rollback and Recovery
• Dual CPLD image (Primary/Backup) used for safe updates.
• Automatic rollback if integrity checks fail.
• Manual recovery options:
- JTAG reflash via recovery jumper.
- BMC or USB-based recovery utility.

## Slide 10: Automation and Fleet Management
• Centralized orchestration via OME, OneView, XClarity, or DCM.
• Sequenced updates: BMC → CPLD → BIOS.
• Parallel but staged rollout for safety.
• Integrated audit and rollback features.

## Slide 11: Best Practices
• Always align CPLD with matching BIOS/BMC versions.
• Avoid updates during power stress or high system load.
• Maintain detailed logs and configuration backups.
• Keep recovery plan and physical access ready.
• Automate using Redfish or Ansible scripts.

## Slide 12: Vendor Tools
Dell – iDRAC, RACADM, OpenManage Enterprise
HPE – iLO, OneView, SUM, Amplifier Pack
Lenovo – XClarity, XCC
Intel – DCM, sysfwupdt, OFU
Supermicro – SUM, IPMItool, SuperDoctor

## Slide 13: Summary Diagram
CPLD Update Flow:
Preparation → Validate → Upload → Flash → Reboot → Validate → Monitor
Include rollback and dependency chain (BMC ↔ CPLD ↔ BIOS).