## Slide 1: Firmware Update Procedure
Ensuring Reliability, Security, and Recoverability

## Slide 2: Overview
• Firmware controls low-level hardware behavior.
• Updates improve functionality, fix bugs, and enhance security.
• A failed update can render hardware inoperable → safety mechanisms are crucial.

## Slide 3: Typical Update Flow
1. Preparation
2. Download & Verification
3. Pre-Update Staging
4. Flashing
5. Verification
6. Reboot & Post-Validation

## Slide 4: Step 1 – Preparation
• Identify target component (BIOS, BMC, NIC, GPU, etc.)
• Verify compatibility (version, hardware ID, model)
• Ensure stable power or redundant PSU

## Slide 5: Step 2 – Download & Verification
• Download firmware binary (.bin, .cap, .rom)
• Verify digital signature and checksum (SHA-256/MD5)
• Secure Boot or BMC validates authenticity

## Slide 6: Step 3 – Pre-Update Stage
• Stop dependent services
• Stage image in RAM or secondary partition
• Use BMC/IPMI for remote orchestration

## Slide 7: Step 4 – Flashing
• Erase old firmware from flash (EEPROM/SPI/NOR)
• Write new image in verified blocks
• Dual-bank (A/B) scheme ensures rollback safety

## Slide 8: Step 5 – Verification
• Bootloader checks hash/signature
• Rollback triggered if mismatch
• Logs recorded in IPMI SEL or journalctl

## Slide 9: Step 6 – Reboot & Post-Validation
• Reboot into new firmware
• Hardware self-tests and version checks
• Health telemetry verified (fans, power rails, PCIe)

## Slide 10: Rollback & Safety Mechanisms
• A/B partitions for recovery
• Watchdog timers for failed boots
• Version pinning to prevent downgrades
• Secure boot chains ensure authenticity

## Slide 11: Tools by Platform
Windows: Dell Command, Lenovo Vantage, HP Support Assistant, FWUpdLcl.exe
Linux: fwupd, flashrom, IPMItool, vendor CLIs
Servers: BMC/Redfish APIs, iDRAC, ILO, IMM
Embedded: DFU, JTAG, OTA pipelines

## Slide 12: Best Practices
• Verify signatures and checksums
• Avoid simultaneous updates
• Maintain detailed logs
• Schedule updates during low load
• Keep rollback images handy
• Use canary rollout for automation

## Slide 13: Summary Diagram
Firmware Update Flow:
Preparation → Download → Pre-Stage → Flash → Verify → Reboot → Validate
(Include rollback and health check paths visually)